## Slide 1: MICRO PROCESSOR & MICRO CONTROLLER
P.RAJESH M.Tech.,
ASST PROFESSOR
DEPT OF ECE
CRIT COLLEGE OF ENGG

## Slide 2: PROCESSOR
A processor is a logic circuitry (or) electronic device responds to and processor the basic instructions that drive a computer.

## Slide 3: MICRO PROCESSOR
Incorporates the functions of a computers central processing unit (CPU) on single IC (or) at most a few IC’s.
(or)
µp is programmable Ic device that has computing and decision making capability
The processor is multipurpose , programmable device that accepts digital data as input processes it according to instructions stored in its memory and provides result as o/p.
(eg:- sequential logic)

## Slide 4
µp is program controlled device which fetches ,decodes , and executes instructions.
The µp reads instructions from memory communicates with all peripherals (memory & i/p ‘s ) using the system bus excepts instruction.
The µp controls the timing of information flow performs the computing tasks specified in a program.

## Slide 5: History of µp
First 4-bit µp 4004 from INTEL corporation in 1971 which has revolution in distal system design.
First 4-bit µp 4004 contained ten thousands (10,000) transistors
After 4-bit µp 4004 ,immediately from INTEL corporation in 1972 first 8-bit µp 8008 which are not successful.
In 1974 from INTEL corporation first 8-bit µp 8080 general purpose µp in which CPU was not functionally successful.
Later on first 8-bit µp 8085 functionally complete CPU introduced in 1977

## Slide 6
The 8085 µp CPU is still most popular one amongst all 8-bit CPU which provides good performance utilizing an optimum set of registers and an reasonably powerful ALU, where 8085 houses on chip clock generator.
The major limitations of 8-bit µp are their limited memory addressing capacity ,slow speed of exception limited scratched register and non availability complex instructions and addressing modes
First 16-bit µp 8086 from INTEL corporation in 1978 which is more powerful efficient computing machine.

## Slide 7: Evolution of µp’s
First 4-bit µp 4004 from INTELL corporation in 1971.
Intel developed an improved 4-bit µp 4004,enchanced versions of intel 4004 many other companies also introceduced 4-bit µp such as PPS-4 by ROCKWELL international ,T3472 by Toshiba etc.,
INTEL corporation in 1972 first 8-bit µp 8008 which so far used PMOS technology these technology of P-MOS used is slow and not compatiable with TTL circuits.
In 1974 from INTEL corporation first 8-bit µp 8080 general purpose µp used N-MOS technology and was faster and compatible with TTL circuits, these NMOS processor offers higher density than PMOS process.
The draw backs of 8080 was that it is required 3-power supplies

## Slide 8
In 1976 Intel introduced 8-bit µp 8085 which required only one +5V power supply.
8-bit µp ‘s are Motorola MC6800,MC6809,Zilogs Z80,Z800
MOS technologies 6500 series , National semiconductors (NSC 800) and Rockwell international PPS-8
First 16-bit µp 8086 from INTEL corporation in 1978.
Some other 16-bit µp are intel 80186,intel 8088,intel 80188,intel 80286, Motorolas MC6800,68010,68012, Fairchild 9440, zilogs Z800, national semi conductor PACE INS8900. these used HMOS (High speed density MOS)technologies.

## Slide 9
HMOS offers better speed power product (SPP) higher packing density than NMOS.
speed power product (spp) = speed * power
                = nanoseconds * mill watts
                = pico joules
spp of HMOS is 4-times better than NMOS
circuitry density provided by HMOS (4128 gates /µm square) are approximately twise these of NMOS (1852 -5 gates/ µm square)
intel 8088 was very popular and was used in costlier and more powerful personal computer

## Slide 10
In 1980 many 32 bits mp’s have been introduced .
Intel introduced its first 32 bits mp IAPX432 not popular
IN 1985 intel introduced more powerful 32 bit Intel 80386 used in desktops
Some other 32- bits mps are INTEL 80486, Pentium, Pentium pro ,Pentium II , Pentium III , Pentium IV,
Advanced Micro Devices (AMD) K5,K6,K7
National semiconductors 32032,32332,32C532
Intel 486 was very popular and widely used for desktops.

## Slide 11
8-bit micro processor | 16-bit micro processor
1. Simple architecture 2. Slow speed of execution 3. Low memory addressing capability 4. Less powerful instruction set 5. Fabricated using PMOS & NMOS technologies 6. applications:- Data acquisitation systems , numerical control ,automatic testing system 7. Limited no:- of general purpose register | Advanced Architecture More processing capability Larger memory addressing capability More powerful instruction set Fabricated using HMOS technologies Applications :- control systems ,traffic controllers, intelligent terminals & instructions 7. More no:- of GPR’s

## Slide 12
Historical processor | Year | Transistor no:- | Clock speed | Address bits | Data bus in bits | Addressable memory
4004 8008 8080 8085 8086 8088 80286 80386 80486 Pentium Pentium pro Pentium II Pentium III Pentium IV | 1971 1972 1974 1976 1978 1979 1982 1985 1988 1993 1995 1997 1999 2000 | 2300 3500 6000 6500 29000 29000 1,34,000 2,75,000 1.3mega 3.1 meg 3.5 meg 8.8 meg 9.5 meg 4.2 meg | 108 Khz 200khz 2 mhz 3 mhz 5 mhz 5 mhz 8 mhz 16 mhz 25 mhz 60 mhz 150 mhz 230 mhz 650 mhz 1.4 ghz | 10 14 16 16 20 20 24 32 32 32 32 36 36 36 | 4 8 8 8 16 8 16 32 32 32/64 32/ 64 64 64 64 | 640 bytes 16 kbytes 64 kbytes 64 kbytes 1 MB 1MB 16 mega 4 giga Giga 4 giga 64 giga 64 giga 64 giga 64 giga

## Slide 13: Register organization of 8086
8086 has powerful set of registers known as
1. general purpose registers and
2. special purpose registers.
All are 16-bit registers
The general purpose registers can be used as either 8-bit OR 16-bit registers which are used for holding data , variable and immediate results temporarily (or) for other purpose like a counter (or) for storing Offset address for particular address.

## Slide 14
special purpose registers.:-
  Used as segment registers , pointers , index registers (or) Offset storage registers for particular addressing.
  The registers are categorized in to 4- GROUPS
  A) GENERAL DATA REGISTERS
  B) SEGMENT REGISTER
  C) POINTERS & INDEX REGISTERS
  D) FLAG REGISTERS

## Slide 15: a) GENERAL DATA REGISTERS
AH (8-bit) | AL(8-bit)
BH(8-bit) | BL(8-bit)
CH(8-bit) | CL(8-bit)
DH(8-bit) | DL(8-bit)
AX(16-bit)
BX(16-bit)
CX(16-bit)
DX(16-bit)
ACCUMULATOR
BASE REGISTER
COUNT REGISTER
DATA REGISTER
AX , BX, CX, DX stands for 16-bit registers used to store data lower
Bits & higher bits.
AH,BH,CH,DH stands for (HIGHER 8- bit registers)
Eg:- A=10,B=11,C=12,D=13,E=14,F=15
AL,BL,CL,DL stands for (LOWER 8-BIT REGISTERS)
Eg: binary bits from (0-9 are lower bit)

## Slide 16
Accumulator is default acts as result storage for arithematic & logical operations .“AX” is a 16-bit ACCUMULATOR with lower 8-bit is designated as ‘AL’ and Higher 8-bit as ‘AH’ .this is most important GPR (general purpose register) having multiple functions.
Base register particularly used in some addressing modes [based addressing modes, relative based addressing , relative indexed addressing modes ]. The ‘BX’ 16-bit register having higher and lower 8-bit (BL, BH) which is used as an Offset storage for forming physical address in case of certain addressing modes.
Counter register is default counter of string , shift ,rotate operation. The ‘CX’ 16-bit register is used as default counter in case of string and loop instructions.
Data register is used to hold I/O ports address which will act as defult destination in case of multiplication & division operation along with AX.The ‘DX’ 16-bit register is used as a implicit operand (or) destination in case of few instructions.

## Slide 17: B) SPECIAL PERPOSE (OR)SEGMENT REGISTER
The complete 1MB of a mp’s 8086 address is divided in to 16-logical segments.
Each segment thus contain 64kbytes of memory
  There are 4 segment registers
Code segment | CS
Stack segment | SS
Data segment | DS
Extra segment | ES

## Slide 18
A) CODE SEGMENT:-
  Is used for addressing a memory location in code segment of the memory where executable program is stored.
B) DATA SEGMENT:-
this type of register points to data segment of the memory where the data is resided.
C) EXTRA SEGMENT:-
this segment which is essential to another data segment of the memory thus Extra segment also contain data.
D) STACK SEGMENT:-
used for addressing stack segment memory i.e.
Memory in which is used to store stack data.
The cpu uses stack for temporarily storing important data

## Slide 19: c) Pointers & index registers
The pointer contain offset within the particular segment.
The pointers & index registers are categorized in to following types .
SP | STACK POINTER
BP | BASE POINTER
SI | SOURCE INDEX
DI | DESTINATION INDEX
IP | INSTRUCTION POINTER

## Slide 20
A)STACK POINTER:-
  Used to hold the offset address b/w starting address of Stack segment to memory location where we are recently stored . Stack top is upper most filled memory location in stack memory. It can be used to store offset address in case of stack segment.
  B) BASE POINTER:-
  Acts as a memory pointer to stack segment register where BP is manly used to access any location directly in the stack.
  C) SOURCE INDEX & DESTINATION INDEX:-
  Index register particularly used in string operation .
  SI used in holding Offset address of source data
  DI used to hold Offset of destination data.
  Acts as memory pointer relative to segment register DS. The mp’s will take Effective address of the data from SI and stores in DI (INDEX register used in string manipulation).
  D) INSTRUCTION POINTER:-
  used to hold address of the next instruction to be fetched that means holds the offset of code segment.
  The offset address of the next instruction is contained in IP . That is IP points to next instruction be fetched from code segment.

## Slide 21: D) Flag registers
The 8086 flag register content indicates the result of compilation in the ALU .
IT contains some flag bits to control the CPU.