## Slide 1: STATUS (OR)FLAGS REGISTERS MICRO PROCESSOR
P.RAJESH M.Tech.,
ASST PROFESSOR
DEPT OF ECE
CRIT COLLEGE OF ENGG

## Slide 2: FLAGS
A FLAG is a flip flop which indicates same condition produced by the excitation of an instruction .
The 8086 mp’s has 16-bit flag register it is also called status register(or) program status word (PSW).
In 16-bit flag register 8086 has 9-FLAGS & remaining are 7-flags bit portions of status register are undefined “(X)”

## Slide 3
In 9-bit flags 6-flags are conditional flags they are SET (or) RESET by the processor depending on the result of some arithmetic & logical operation.
The 6-conditional flags are CF,PF,AF,ZF,SF,OF
THE 3-flags are control flags these are set (or) Reset by programmer as required by certain instructions in a program.
The control flags are TF,DF,IF

## Slide 4
X | X | X | X | OF | DF | IF | TF | SF | ZF | X | AF | X | PF | X | CF
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
8085 MICRO PROCESSOR
COMPATIABLE FLAGS
X  DEFINED AS “UNDIFIEND”
7-BIT OF PORTIONS OF STATUS REGISTERS
6- CONDITIONAL FLAGS
CF  CARRY FLAG
PF  PARITY FLAG
AF  AUXILARY FLAG
ZF  ZERO FLAG
SF  SIGN FLAG
OF  OVER FLOW FLAG
3 - CONTROL FLAGS
DF  DIRECTION FLAG
IF  INTERUPT ENABLE FLAG
TF  TRAP FLAG

## Slide 5: 6- CONDITIONAL FLAGS
CF  CARRY FLAG
PF  PARITY FLAG
AF  AUXILARY FLAG
ZF  ZERO FLAG
SF  SIGN FLAG
OF  OVER FLOW FLAG

## Slide 6
CF  CARRY FLAG
This flag is set when ever a CARRY/ Barrow occurs during arithmetic operation such as addition (or) subtraction other wise it is reset.
PF  PARITY FLAG
  This flag is set ‘1’ if the lower byte of the result contains even number of 1’s.
  If the lower byte of result contains Odd number then parity flag is Set as ZERO(“0”)

## Slide 7
AF  AUXILARY FLAG
  this is set if there is a carry from the lowest nibble.
  Eg:- Bit three during addition of barrow for lowest nibble (4-bit)
  Eg:- Bit three during subtraction in to (2-bits)
SF  SIGN FLAG
This flag is set when the result of any computation is negative.
if the flag is set if MSB of the result is zero.
if the set to zero if the MSB of result is zero
ZF  ZERO FLAG
This flag is set if the result of an arithmetic (or) logic operation is zero . In case of non zero result this flag is set zero.

## Slide 8
OF  OVER FLOW FLAG
  This flag is set if an overflow occurs i.e. if the result of a signed operation is large enough to be accommodated in a destination register overflow flag has no significance in unsigned operation.

## Slide 9: CONTROL FLAGS
TF  TRAP FLAG
IT is used for single step control . If this flag is set the processor enters the single step execution mode.
IT allows user to execute once instruction of a program at a time for debugging.
IF  INTERUPT ENABLE FLAG
IT is a interrupt enable /disable flag .If thi is set the mask able interrupt are recognized by the CPU, otherwise they are ignored.

## Slide 10
DF  DIRECTION FLAG
IT is used by string manipulation instructions if this flag bit is ‘0’ the string is processed beginning from the lowest address to the highest address i.e. auto incrementing mode otherwise the string is processed from the highest address towards lowest address i.e. auto decrementing.