## Slide 1: Procedures and Macros
P.RAJESH M.Tech.,
Assitant Professor
CRIT engg college

## Slide 2: Procedures:
When a group of instructions are to be used several times to perform a same function in a program, then we can write them as separate subprogram called procedure or subroutine.
Procedures can be called in a program using CALL instructions.
Procedures are written and assembled as separate program modules and stored in the memory. The assembling of procedures will be done without considering the main program i.e., independent of calling program.

## Slide 3
Label PROC Far / Near
------
------
RET Label ENDP.
When procedure is called in main-program control is transferred to procedure and after execution the control is transferred back to main program, procedures are called using CALL instruction and returned back using RET instruction.

## Slide 4
Types of Procedures:
  Depending on Position of procedure in memory
    Intra-segment Procedure
    Inter-segment Procedure
  Depending on occurrence in program
    Single Procedure
    Nested Procedure
    Re-Cursive Procedure
    Re-Entrant Procedure

## Slide 5
Intra-Segment Procedure:
CALL  (SP)  (SP) – 2
((SP) + 1 : (SP))  (IP)
(IP)  (EA)
RET  (IP)  ((SP) + 1 : (SP))
(SP)  (SP) +2

## Slide 6
Inter-Segment Procedure:
CALL  (SP)  (SP) – 2
(((SP) + 1) : (SP))  (CS)
(SP)  (SP) –2
(((SP) + 1) : (SP))  (IP)
(IP)  (EA)
  (CS)  Seg. Address
RET  (IP)  ((SP) + 1 : (SP))
(SP)  (SP) – 2
(CS)  ((SP) + 1 : (SP))
(SP)  (SP) – 2
Single Procedure:
MP  Main Program
SP  Sup-Program / Procedure
MP
CALL
RET
SP

## Slide 7
Nested Procedure
CALL
CALL
RET
RET
MP
SP1
SP2

## Slide 8
Re-Cursive Procedure:
CALL
CALL
RET
RET
MP
SP1
SP1
SP1
CALL
RET

## Slide 9
The recursive procedures are implemented using procedure CALL itself, but care must be taken to assure that each successive call does not destroy the parameters and results generated by the previous CALL and make sure that procedure does not modify itself, i.e., each call must store its set of parameters, Registers and all temporary results in a different place in memory.
Push all the flags and all registers used in the procedure.
Should use only register or stack to pass parameters.

## Slide 10
Re-Entrant Procedures:
ISR
SP
MP
INT
CALL
RET
IRET
CALL SP

## Slide 11: MACROS:
When a group of instructions are to be used several times to perform a same function in a program and they are too small to be written as a procedure, then they can be defined as a MACRO.
A MACRO is a small group of instructions enclosed by the assembler directives MACRO and ENDM.
The MACROS are identified by their names and usually defined at the start of a program.
The Macro is called by its name in the program, whenever the MACRO is called in the program, the assembler will insert the defined group of instructions in place of CALL instruction.

## Slide 12
X1 MACRO
Mov SI, OFFSET Arr
Mov DI, OFFSET Arr1
Mov AL, (SI)
Add AL, (DI)
Inc SI
Inc DI
ENDM

## Slide 13
Passing parameters in MACROS:
X1 MACRO Arr, Arr1
:
END M
:
X1 Arr2,Arr3
:
X1 Arr4, Arr5

## Slide 14: Advantages and Disadvantages Of Procedures and Macros:
Procedures: Advantages:
1. Machine codes for the group of instructions in the procedure has to be put in memory only once.
2. Each set of instructions can be individually assembled and debugged.
Disadvantages:
1. Need stack operations performed.
2. Over-head time required to call the procedure and return to the calling program.

## Slide 15
Macros Advantages:
1. Simple
2. No over-head time required.
Disadvantages:
Program may take up more memory due to insertion of machine codes in the program at the place of Macros.

## Slide 16
S.No. | Procedures | Macros
1. | Machine code for instructions are stored in memory only once. | Machine codes are generated for instructions in the Macro each time it is called in the main program.
2. | Accessed by CALL and RET mechanisms during program execution. | Accessed during assembly with name given to Macro when defining it.
3. | Size is unlimited. | Size is limited to few lines.
4. | Parameters are passed in registers, Memory locations or stack. | Parameters are passed as part of statement which calls Macro.
5. | Can be present in Same (or) different segment as that of the main program. | Usually defined at the beginning of program in the same segment.